## Slide 1: MADINAS Use Cases
S. Ringland (BT)
Rajat Ghai (Comcast)
M. Boucadair (Orange)

## Slide 2: Diagnostics
Internet Service Providers need to be able to provide remote support for their customers to help identify and diagnose problems that the customers are having with their Wi-Fi.
To enable this, the ISPs need to be able to identify the current performance and behaviour of each individual device and to understand the patterns of performance of each device over a period of time that extends to at least several weeks.
The ISPs, therefore, need a persistent device identifier. For most diagnostics purposes the identifier only needs to be unique and persistent within an individual home network (ESS). However, there exist some diagnostics examples (such as detecting when a device has mistakenly connected to the community Wi-Fi side of an access point rather than the private LAN side), where an identifier that is common across different ESSes would be required.
The ISPs also need to be able to discuss the performance of specific identified devices with the customer and so need to be able to tie the diagnostic device identifier to a device name or description that the customer will understand.

## Slide 3: Legacy Client Steering and Pre-Association Steering
While the new MBO based client steering relies on devices reporting their view on the signal strengths of access points, legacy mechanisms rely on access points making measurements of the signal strength of clients.
For such solutions, access points may have to compare the signal strength they see on a probe request on one band with the signal strength they see for data traffic of the same station that is associated on another band.
If the probe request uses a different MAC address than is used for the associated connection, then the access point will be unable to determine that the probe request is from the same device and will therefore be unable to perform the client steering action.
Furthermore, APs may need to record which clients do not respond well to legacy steering attempts in order to avoid repeating the same poor experience. This requires a persistent identifier for the client device.
Pre-association steering may also be impacted, depending on the specific implementation, as client devices using MAC randomisation may use one MAC address for probing and a different one for association.

## Slide 4: MAC address Access Control
There exists implementations that rely on MAC address filter for access control.
Examples:
  ISPs use MAC address filter to mitigate DDOS at the L2 edge
  Many home gateways provides MAC address filter function for access control such as White List and Black List

## Slide 5: Sticky DHCP Assignment for Incoming Access
Many gateways provide dhcp server service. It is quite common users will use sticky DHCP assignment to set a fixed IPv4 address for various functions:
  DMZ
  Port-Forwarding

## Slide 6: Community Wi-Fi Auto Sign-on
Many ISPs offer an open and secure SSID as a public wifi service to their customers across millions of APs.
Many users access public Wi-Fi service use the open SSID.
First time Authentication of a user is done via username/password provided by the supplicant.
Once the identity of the user is confirmed and verified the network caches the MAC address of the supplicant for provide auto auth to return users, until cache expiry.
Randomization of the device MAC breaks the auto-signon convenience and our subscribers have to sign-on at MAC refresh.

## Slide 7: QoE measurement/Improvement
Some Community WiFi providers do continuous measurement of Quality Of Experience (QoE) of their users on the WiFi network by scoring the QoE
Correlation of QoE experiments pre / post network tuning is done using device MACs ; This is an iterative process that relies on a persistent device identifier (MAC). e.g.
  Device MAC A had a QoE score of X.
  Operations team tunes that segment of the network, soak changes
  After Y days, QoE measurements are performed for Device MAC A , and QoE score of X’ is observed.
  Such iterative QoE improvement operations break with MAC randomization.

## Slide 8: Enhanced Features for Home Network (Plume)
A device in home is associated to a family member profile using the device’s MAC address
Following features are based on the family profile (affected by MAC address randomization):
  Security and content access policies (Ex- Adult content access restriction on a child device)
  Pause or freeze schedules (Ex- Dinner time or Bedtime internet restriction for family members)
Device nicknaming, person or room assignment is also lost

## Slide 9: Cloud Resource Management (Plume)
A device record is stored in cloud for management of various features (family profile, service policies, steering, etc)
The size of the record database increases astronomically as the device MAC address change frequency reduces (Ex. For one month period, if the MAC address of each home client changes every 24 hours, then database size is 30X more than that of one where no device randomized MAC address once associating to the network)
This also results in increase in complexity of database management as well as other essential cloud components referring the device records

## Slide 10: Summary
Following use-cases are affected by MAC address randomization:
  Diagnostics data for measuring device performance or validating regular device behavior will be inadequate for analysis
  Legacy client steering and pre-association steering
  MAC access control based features- DDoS attack prevention, white-listing/black-listing features for home network
  Sticky DHCP IPv4 assignment for DMZ and port-forwarding
  Community WiFi auto sign-on across ISP network
  QoE measurement and continuous feedback based improvement
  Enhanced features for home network (family profile, security policies, internet pause)
  Cloud resources and complexity grows with the frequency of MAC randomization