## Slide 1: MADINAS Use Cases
S. Ringland (BT)
Rajat Ghai (Comcast)
M. Boucadair (Orange)

## Slide 2: Diagnostics
Internet Service Providers need to be able to provide remote support for their customers to help identify and diagnose problems that the customers are having with their Wi-Fi.
To enable this, the ISPs need to be able to identify the current performance and behaviour of each individual device and to understand the patterns of performance of each device over a period of time that extends to at least several weeks.
The ISPs, therefore, need a persistent device identifier. For most diagnostics purposes the identifier only needs to be unique and persistent within an individual home network (ESS). However, there exist some diagnostics examples (such as detecting when a device has mistakenly connected to the community Wi-Fi side of an access point rather than the private LAN side), where an identifier that is common across different ESSes would be required.
The ISPs also need to be able to discuss the performance of specific identified devices with the customer and so need to be able to tie the diagnostic device identifier to a device name or description that the customer will understand.

## Slide 3: Legacy Client Steering and Pre-Association Steering
While the new MBO based client steering relies on devices reporting their view on the signal strengths of access points, legacy mechanisms rely on access points making measurements of the signal strength of clients.
For such solutions, access points may have to compare the signal strength they see on a probe request on one band with the signal strength they see for data traffic of the same station that is associated on another band.
If the probe request uses a different MAC address than is used for the associated connection, then the access point will be unable to determine that the probe request is from the same device and will therefore be unable to perform the client steering action.
Furthermore, APs may need to record which clients do not respond well to legacy steering attempts in order to avoid repeating the same poor experience. This requires a persistent identifier for the client device.
Pre-association steering may also be impacted, depending on the specific implementation, as client devices using MAC randomisation may use one MAC address for probing and a different one for association.

## Slide 4: MAC address Access Control
There exists implementations that rely on MAC address filter for access control.
Examples:
  ISPs use MAC address filter to mitigate DDOS at the L2 edge
  Many home gateways provides MAC address filter function for access control such as White List and Black List

## Slide 5: Sticky DHCP Assignment for Incoming Access
Many gateways provide dhcp server service. It is quite common users will use sticky DHCP assignment to set a fixed IPv4 address for various functions:
  DMZ
  Port-Forwarding

## Slide 6: Community Wi-Fi Auto Sign-on
Many ISPs offer an open and secure SSID as a public wifi service to their customers across millions of APs.
Many users access public Wi-Fi service use the open SSID.
First time Authentication of a user is done via username/password provided by the supplicant.
Once the identity of the user is confirmed and verified the network caches the MAC address of the supplicant for provide auto auth to return users, until cache expiry.
Randomization of the device MAC breaks the auto-signon convenience and our subscribers have to sign-on at MAC refresh.

## Slide 7: QoE measurement/Improvement
Some Community WiFi providers do continuous measurement of Quality Of Experience (QoE) of their users on the WiFi network by scoring the QoE
Correlation of QoE experiments pre / post network tuning is done using device MACs ; This is an iterative process that relies on a persistent device identifier (MAC). e.g.
  Device MAC A had a QoE score of X.
  Operations team tunes that segment of the network, soak changes
  After Y days, QoE measurements are performed for Device MAC A , and QoE score of X’ is observed.
  Such iterative QoE improvement operations break with MAC randomization.