## Slide 1: MADINAS Use Cases
Simon Ringland (BT)
Rajat Ghai (Comcast)
Ian Wheelock (Commscope)
Mohamed Boucadair (Orange)
Malay Vadher (Plume)
Ajay Manuja (Benu Networks)

## Slide 2: Access Control based on MAC Addresses
CPEs widely support filtering features based MAC addresses
  An additional guard for access control such as accept- or discard-lists
Example services:
  ISPs use MAC address filter to mitigate DDoS at the L2 edge. Filtering based on the IP address at the network side is suboptimal
  Schedule when a device can be granted access (e.g., parental control)
  Seek a confirmation from an administrator when a new device is detected

## Slide 3: Sticky DHCP Assignment for Incoming Connections
CPEs provide DHCP server service
It is quite common that users rely upon a sticky DHCP assignment to assign a static IPv4 address to a given device for various functions:
  DMZ
  (Static) Port Forwarding

## Slide 4: DHCP Address Pool Exhaustion
Clients connecting with different MAC addresses are assigned new DHCP IP addresses
Normally a DHCP Server maintains a single IP address for a client
With MAC Randomisation, the DHCP Server has to assign a new IP address every time a client changes its MAC address
IP Address exhaustion at the DHCP server may prevent clients from joining a network as no more addresses free to assign
If customer network equipment is limited to a maximum number of MAC addresses, this may be exhausted due to MAC randomisation

## Slide 5: Diagnostics
ISPs need to be able to provide remote support for their customers to help identify and diagnose problems that the customers are having with their connectivity.
There is a need to be able to identify the current performance and behaviour of each individual device and to understand the patterns of performance of each device over a period of time that extends to at least several weeks.
Thus there is need for a persistent device identifier.
  For most diagnostics purposes the identifier only needs to be unique and persistent within an individual home network (ESS).
  However, there exist some diagnostics examples (such as detecting when a device has mistakenly connected to the community Wi-Fi side of an access point rather than the private LAN side), where an identifier that is common across different ESSes would be required.
ISPs also need to be able to discuss the performance of specific identified devices with the customer and so need to be able to tie the diagnostic device identifier to a device name or description that the customer will understand.

## Slide 6: Cloud Resource Management
A device record is stored in cloud for management of various features (family profile, service policies, steering, etc)
The size of the record database increases astronomically as the device MAC address change frequency reduces (Ex. For one month period, if the MAC address of each home client changes every 24 hours, then database size is 30X more than that of one where no device randomized MAC address once associating to the network)
This also results in increase in complexity of database management as well as other essential cloud components referring the device records

## Slide 7: Community Wi-Fi Auto Sign-in
Many ISPs offer an open and secure SSID as a public Wi-Fi service to their customers across millions of APs
Many users access public Wi-Fi service using the open SSID
  First time authentication of a user is done via username/password provided by the supplicant
  Once the identity of the user is confirmed and verified the network caches the MAC address of the supplicant for provide auto auth to return users, until cache expiry.

## Slide 8: QoE Measurement & Improvement
Some Community Wi-Fi providers do continuous measurement of Quality Of Experience (QoE) of their users on the Wi-Fi network by scoring the QoE
Correlation of QoE experiments pre/post network tuning relies upon a persistent device identifier (MAC). For example:
  Device MAC “A” had a QoE score of “X”
  Operations team tunes that segment of the network, soak changes
  After Y days, QoE measurements are performed for device MAC “A” , and QoE score of “Z” is observed

## Slide 9: Legacy Client Steering and Pre-Association Steering
While the new MBO based client steering relies on devices reporting their view on the signal strengths of access points, legacy mechanisms rely on access points making measurements of the signal strength of clients.
For such solutions, access points may have to compare the signal strength they see on a probe request on one band with the signal strength they see for data traffic of the same station that is associated on another band.
If the probe request uses a different MAC address than is used for the associated connection, then the access point will be unable to determine that the probe request is from the same device and will therefore be unable to perform the client steering action.
Furthermore, APs may need to record which clients do not respond well to legacy steering attempts in order to avoid repeating the same poor experience. This requires a persistent identifier for the client device.
Pre-association steering may also be affected, depending on the specific implementation, as client devices using MAC randomisation may use one MAC address for probing and a different one for association.

## Slide 10: Enhanced Features for Home Network
A device in home is associated to a family member profile using the device’s MAC address
Following features are based on the family profile (affected by MAC address randomization):
  Security and content access policies (Ex- Adult content access restriction on a child device)
  Pause or freeze schedules (Ex- Dinner time or Bedtime internet restriction for family members)
Device nicknaming, person or room assignment is also lost

## Slide 11: Community Wifi Mobility Event
Broadband
Access
Internet
New Device onboarding
  AP tunnels all traffic to WAG
  Portal or MAC based Auth via AAA
  WAG Assigns local IP Address and NAT ports
Mobility Event – UE move between APs
  UE MAC is matched to detect the tunnel switch at WAG
  UE IP and NAT state is switched to new AP
Different MAC from same UE
  Restart of device onboarding and Authentication process
  Reset of all existing connections and NAT pool
  Possible service denial attack If MAC is not checked
AAA
WAG

## Slide 12: Use Case Summary
Today many services rely on the device MAC address being a persistent identifier
The consequence of the introduction of MAC randomisation is that these services will stop working
Alternative identity solutions are required to enable the services to continue to operate whilst preserving user privacy
Requirements
Different use cases have different requirements on an identity, so a number of different solutions may be required.
Key features to consider for each case are shown in the table to the right ==>
Example Use Cases
Access Control
Sticky DHCP Assignment
DHCP Address Pool Exhaustion
Diagnostics
Cloud Resource Management
Community Wi-Fi Auto Sign-in
QoE Measurement & Improvement
Legacy Client Steering
Pre-Association Steering
Enhanced features for home network
Feature | Description
Persistence | How long must the identifier persist?
Security & Trust | What level of trust is required between the client and the network and how confident must the network be that the client is the true owner of the identity?
Pre-Association Security & Trust | Is the same identifier required to be used pre- and post-association?
Single, multiple or all SSIDs | Is the same identifier required on a single network (ESS) or multiple networks?
Device or User | Does the identifier represent the device or the user?
Mandatory or user opt-in | Must the identifier be provided in order to join the network, or must the user opt-in?
Provisioning | The provisioning of any new identifier must be low-friction for the user. How could this be achieved?